## Slide 1: Magnetometer Editor

## Slide 2
Magnetometer Editing
New Interface is designed around the Magnetometer data

## Slide 3: Docking ability of Windows
The windows can be docked to various areas of the editor.

## Slide 4: Left Menu Area
Remove File from Session
Common HYPACK Tool set to edit data
Tabs to view the data can be directly accessed or selected through the menu
Open and Save Session
New tools for Contouring and Sorting in the Editor

## Slide 5
MAG EDIT Supports:
  Stand-alone magnetometers.
  Stand-alone magnetometers with IGRF corrections.
  Sea magnetometer with Shore Based magnetometer, both with IGRF corrections.
Magnetometer Editing

## Slide 6: Shore Data Tools
IAGA positions are provided in co-latitude: the difference between the latitude and 90°
The time shift to accommodate the distance between the boat and shore station. If shore data is at a different time interval than the raw data, the MAGNETOMETER EDITOR interpolates the shore data to calculate values to match the raw data
The elevation is provided for IAGA stations

## Slide 7: New Session Methodology
HYPACK 2020 Magedit reads HYPACK Raw files and saves to XYZ or a Session File per line with a LOG File.
XYZ data can be taken into the TIN MODEL program to generate a color filled DXF or 3d Displays.
The new Session file is a BINARY file which contains the corrections and raw information to allow users to visualize the corrections applied.
Using the Binary file format the file size is smaller and loads quicker while containing more information.

## Slide 8
Editing Tools
Gamma values in Profile Window

## Slide 9
Target Tool – Whole Magnetic Analysis
To target an area, click and drag with the left mouse button around the area you wish to mark.
Information about the target will appear in a new window.
Click “Mark Target” to save the data to the target database.

## Slide 10
Target Tool – Whole Magnetic Analysis
Write to RTF will create an image of the display and add it to a RTF file that can be used as a target report.
Target location and name
Target properties

## Slide 11
Mag Edit Report in RTF – Rich Text Format

## Slide 12
Spreadsheet - Layout
Recommended Shore Layout Button

## Slide 13
Spreadsheet
Raw Anomaly: Gamma1 – IGRF(Boat)
Diurnal Component: Shore Filter –(IGRF (Shore) + Station Constant)
Agitation Component: Unshifted Shore – Unshifted Filter
Diurnal Anomaly: Gamma 1 - IGRF(Boat) - Diurnal Component
Total Anomaly: Gama 1- IGRF(Boat)- (Diurnal Component – Agitation Component)
Vessel with Shore-Based Adjustments

## Slide 14
Spreadsheet –
Vessel with Shore-Based Adjustments
Boat
Gamma 1: Measurement with no corrections
IGRF(Boat): IGRF adjustment for boat
Raw Anomaly: Gamma 1 – IGRF (Boat)
Shore
Time Shift: Latency correction between the ship and the shore station
Shore Value: Gamma value of shore station or IAGA at shifted time
Shore Filter: 5 hours filter on shore value
IGRF (Shore): IGRF adjustment for shore station at shifted time
Station Constant: Station magnetic field average
Diurnal Component: Diurnal variation at shifted time
Unshifted Shore: IGRF adjustment for shore station at unshifted time
Unshifted Filter: Gaussian filter on unshifted time
Agitation Component: high frequency component
Diurnal Anomaly
Total Anomaly

## Slide 15
Standalone Magnetometer with IGRF Corrections
Raw Anomaly = Raw Gamma – IGRF Boat
The Raw Anomaly is the difference in the readings from the magnetometer and the calculated earth’s magnetic field at the location (IGRF)
Each sample has a calculated IGRF value. This calculation can take several minutes to calculate.
IGRF Boat
Sample location
and time
IGRF Model
Standalone Magnetometer with IGRF Corrections

## Slide 16
*Shore based data could be input in SHOM or IAGA Formats
Station Constant = Average Shore Based Data – Average IGRF (Shore Based Data)
IGRF Shore
Shore Based DATA*
IGRF Model
Shore-Based Magnetometer with IGRF Corrections

## Slide 17
Diurnal Component: Oscillations of the earth's magnetic field that:
Have a periodicity of about a day
Depend only on local time and geographic latitude.
Diurnal Anomaly =
Shore Filter*- (IGRF (Shore)+Station Constant)
* 5 hours Filter
The variation is calculated with a time shift as this variation is not simultaneous. It depends on the longitude difference between the ship and the shore station.
Delta t = 240* [longitude (ship) – longitude (shore-based)]
Shore-Based Magnetometer with IGRF Corrections

## Slide 18
Downloading INTERMAGNET data
http://intermagnet.org/data-donnee/download-eng.php
Select the date of your survey, select the station, and download the file.

## Slide 19
Variation of magnetic fields caused by solar activity are considered simultaneous for the ship and the shore station
Agitation Component = Unshifted Shore Base Data - Unshifted Filtered* Shore Base Data
*5 hours Filter
Shore-Based Magnetometer with IGRF Corrections

## Slide 20
With Shore-Based Reference Station and IGRF Corrections
Reference station can be user-supplied or IAGA station
Separate IGRF values are computed for both vessel and shore-based measurements
5 hour filter is applied on Shore Based Data
Time Shift is applied to the Diurnal Component
Unshifted Value is applied to Agitation Component
Shore Based data and results calculation could be display in color
Spreadsheet

## Slide 21
Stand Alone Mode
No IGRF corrections
NO shore-based magnetometer
Stand Alone Mode with IGRF Corrections
IGRF corrections
NO shore-based magnetometer
Values are large
Values are small
Spreadsheet

## Slide 22
Display recommended information
Spreadsheet

## Slide 23
SURVEY Window
Displays track lines and background chart A marker indicates your current position Use this to correlate anomalies with features on the charts All charts displayed in the shell will show up here

## Slide 24
Profile Window IGRF Correction
Trackline
Gamma

## Slide 25
Allows for editing of outliers of gamma values, raw anomalies (blue), and/or total anomalies (red)
Profile Window –
With Shore-Based Magnetometer Applied

## Slide 26
MAG EDIT – Default Edited Extension
*.MAG
*.RAW
Mag Edit

## Slide 27
Edited Gamma Value Raw Anomaly Total Anomaly
MAG EDIT

## Slide 28
Save in XYZ format or to new binary Session format.
MAGEDIT Save Options

## Slide 29: Magedit – Generating Contour
The Magedit program now has the ability to generate contours within the program.
Select the Contour button
If you haven’t saved the data you will be prompted to
The Contour Dialog will appear and allow the user to generate contours without opening the Tin Model program.

## Slide 30: Magedit – Sorting Routines
The Magedit program now has the ability to Sort Data within the program.
Select the Sort button
If you haven’t saved the data you will be prompted to.
The 2D Sort option dialog will appear allowing the user to sort the gamma readings for display.

## Slide 31
Tin Model – Generating Contours
Creating a Tin Model of the data allows the user to generate a DXF map of the gamma contours

## Slide 32: Raw Anomaly Allows Better Representation

## Slide 33
GeoTIF created in HYPACK TIN MODEL displayed on top of S-57 nautical chart in the HYPACK SHELL.
Data Presentation

## Slide 34
Export of anomaly contours to Google Earth
Data Presentation

## Slide 35
Smooth sheets can be sent to printer/plotter, GeoTIF, DXF or PDF.
Data Presentation: Mag Anomalies

## Slide 36: Thank You !
January 2020
HYPACK on Youtube.com ( Historical Sessions ) HYPACK Live Chat
HYPACK on Youtube.com ( Newer Sessions ) HYPACK Ustream
HYPACK SUPPORT Site HYPACK Website
Links to more information:
Contact Us:
Sales@HYPACK.com
Help@HYPACK.com
(860) 635 - 1500